## Slide 1
Progress of HM and POP modelling: main activities and results
Alexey Gusev, Ilia Ilyin, Olga Rozovskaya, Victor Shatalov, Oleg Travnikov
Meteorological Synthesizing Centre - East

## Slide 2
Case studies of HM pollution on national scale
Evaluation of B(a)P pollution in urban areas
Assessment of long-term trends in HM and POP pollution
Development of GLEMOS modelling system
Transition of modelling to the new EMEP grid
Co-operation with WGE, CEIP and TFEIP
Cooperation with international bodies
Outline of main activities of MSC-E

## Slide 3
Analysis of Pb pollution levels in Belarus
Multi-model study of Pb pollution for the UK
Analysis of Cd pollution in Poland
Case studies of HM pollution on national scale: assessment of contamination with fine spatial resolution
Recent and ongoing activities (2015-2017):
Belarus
UK
Poland
Main outcomes and benefits:
Improvement of agreement between modelled and observed pollution levels
Better reproduction of small-scale effects (e.g., orographic precipitation)
Improvement of parameterization of wind re-suspension
Analysis of pollution using more detailed national emission and monitoring data

## Slide 4
Evaluation of B(a)P pollution in urban areas
Significant part of urban population in Europe live in areas with exceedances of limit values for B(a)P air concentrations
About half of urban/suburban monitoring stations in Europe measuring B(a)P in air indicate concentrations above the EU target value 1 ng/m3 (EEA, 2015)
Objective of this activity is to estimate B(a)P pollution levels in urban areas of EMEP countries and provide information for exposure studies
Observed B(a)P air concentrations in 2013 (EEA Airbase)
EU target value
Czech Republic

## Slide 5: Long-term trends of HMs and POPs
Trend evaluation for the whole EMEP domain and particular countries based on model calculations
Non-linear character of the pollution trends was investigated (methodology of analysis was elaborated and applied)
Reduction of HMs and B[a]P in the EMEP region, EU28 and EECCA countries
Trends in B[a]P air concentrations in the EMEP countries
-40
-20
0
20
40
60
80
100
Pb
Cd
Hg
B[a]P
Total redcution, %
EMEP
EU28
EECCA
Contribution to CLRTAP, WGE and TFMM Assessments-2016

## Slide 6
Application of moss concentrations data with fine resolution to analysis of pollution levels in co-operation with WGE
29th TF meeting of the ICP-Vegetation, Dubna, Russia, March 2016
Reduction (%) of Pb modelled deposition
Reduction (%) of Pb observed conc. in mosses
Moss measurements (2010)
Lead in mosses
Long-term trends of HMs

## Slide 7
Anthropogenic
emissions
Atmosphere
Land
Ocean
Human & environment
exposure (CCE)
Meteorology,
ocean data
Geophysics
Atmospheric
deposition
Concentration
in media
Global EMEP Multi-media Modelling System (GLEMOS)
Main activities:
Transition of modelling system to new EMEP grid
Improvement of model performance of mercury pollution assessment
Further development and testing of multi-media approach for POPs
Update of open-code version of GLEMOS model
GLEMOS – EMEP model for evaluation of HMs and POPs at global/regional/national scales
GLEMOS general scheme
Further development of HM and POP modelling approach

## Slide 8
Current and new EMEP domains
Current EMEP domain
New EMEP domain
Transition to the new EMEP grid
Current activities on implementation of the new grid:
Data preparation on chemical reactants in the atmosphere
Generation of meteorological data (time series)
Preparation of emissions data based on expert estimates (official data is not available)
Pilot simulations and evaluation against measurements

## Slide 9
Transition to the new EMEP grid
Pilot simulations of Hg pollution over the new EMEP grid (2014)
Hg wet deposition (new EMEP grid)
Hg wet deposition (old EMEP grid)

## Slide 10
Hg0 air concentration
Transition to the new EMEP grid
Evaluation of modelling results vs. EMEP measurements
Hg wet deposition
 | Old grid | New grid
Correlation | 0.72 | 0.92
Regression | 1.40 | 1.35
 | Old grid | New grid
Correlation | 0.63 | 0.60
Regression | 1.06 | 1.11

## Slide 11
Information on HM (Pb, Cd, Hg) and POP (PAHs, HCB, PCBs, PCDD/Fs) emissions | Official emission data (CEIP) | Emission data required for modeling (MSC-E)
Time-series of national total emissions (annually) | X | 
Gridded sectoral emissions (once in five years) | X | 
Emissions of Large Point Sources (once in five years) | X | 
Gridded total emissions for the latest reported year generated by CEIP (except PCBs) (annually) | X | 
Time-series of gridded annual emissions 1990-2012 |  | X
Vertical distribution of emissions |  | X
Speciation of Hg forms (Hg˚, Hg(II)gas, Hg(II)part) |  | X
Congener composition for POPs (PCDD/Fs – 17 congeners, PCBs) |  | X
Temporal variation of emissions |  | X
Historical emissions of PCBs, HCB, PCDD/Fs up to 1990 |  | X
Emissions to other environmental compartments (PCDD/Fs, HCB) |  | X
Emissions for non-EMEP countries within the EMEP domain (North Africa and Middle East) |  | X
Natural emissions |  | X
Re-suspension, re-emissions |  | X
Global emission inventories (PCDD/Fs, HCB, PCBs, Hg) |  | X
Emission data required for model assessment of pollution:
(MSC-E contribution to the joint CEIP/MSC-E technical report)
Development of emission preparation strategy: co-operation with CEIP and TFEIP

## Slide 12
Emission parameter | Pb and Cd | Hg | PAHs | PCDD/Fs and PCBs | HCB
Quality of gridded anthropogenic emissions | 1 | 2 | 1 | 1 | 2
Chemical composition | - | 1 | - | 2 | -
Temporal variation | 2 | 6 | 2 | 6 | 5
Vertical distribution | 3 | 7 | 3 | 7 | 6
Global emissions inventory | 4 | 3 | 4 | 3 | 3
Historical emissions | 5 | 4 | 5 | 4 | 1
Emissions to other media | 6 | 5 | 6 | 5 | 4
- First priority - Second priority - Third priority |  |  |  |  | 
Key emission parameters affecting quality of model estimates
Priorities for emission data preparation for modelling

## Slide 13
Hg measurement data from various monitoring networks (GMOS, NADP/MDN, AMNet, NAtChem)
Hg emissions data (AMAP/UNEP global Hg inventory for 2010, EGDARv4 global Hg inventory for 1970-2008)
Location of monitoring sites
Hg0 concentration in air
Wet deposition
Hg oxidized species in air
Hg anthropogenic emission in 2010 (UNEP)
Global data on mercury emissions and pollution:
Assessment of mercury pollution in the EMEP region: co-operation with international bodies
Notes: 13
13

## Slide 14
TF HTAP Workshop, Potsdam, Germany, February 2016
Participating models: | 
Model | National experts
GLEMOS | EMEP/MSC-E
ECHMERIT | CNR-IIA (Italy)
CMAQ-Hg | HZG (Germany)
WRF-Chem | CNR-IIA (Italy)
GEOS-Chem | MIT (USA)
GEM-MACH-Hg | Environment Canada
p-TOMCAT | Cambridge (UK)
Environment Canada
GEOS-Chem
ECHMERIT
GEM-MACH-Hg
GLEMOS
Multi-model assessment of global mercury pollution and processes
Notes: 14

## Slide 15: Study of Hg atmospheric chemistry
Seasonal variation of Hg wet deposition
Measurements
ECHMERIT
GLEMOS
GEM-MACH-Hg
GEOS-Chem
Sites measuring Hg wet deposition
0
20
40
60
80
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Wet deposition, ng/m
2
/day
99 sites
0
20
40
60
80
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Wet deposition, ng/m
2
/day
Hg0 + Br
0
20
40
60
80
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Wet deposition, ng/m
2
/day
Hg0 + O3
0
20
40
60
80
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Wet deposition, ng/m
2
/day
Hg0 + OH

## Slide 16
Simulated Hg deposition flux (2010)
Source apportionment of Hg anthropogenic deposition
0
2
4
6
8
10
12
Average Hg deposition, g/km
2
/y
Europe
Africa
Middle East
North America
Central America
South America
South Asia
East Asia
Southeast Asia
Australia and NZ
CIS countries
Antarctica
Arctic
Source/receptor regions
Assessment of mercury pollution on global scale
EMEP region
Notes: 16

## Slide 17
Participation in the Global Mercury Assessment 2013 (GMA 2013) to support negotiations of the Minamata Convention on Mercury.
Coordination of work on the update of GMA 2013 with new modelling results (2015)
Leading preparation of the modelling part of Global Mercury Assessment 2018
Contribution to UNEP Global Mercury Assessment
Project Coordination Group of GMA 2018 (Geneva, April 2016)

## Slide 18
Global data on emissions and measured pollution levels of POPs in air and media
PCDD/F emissions of more than 140 countries (based on UNEP Emission Toolkit)
Emission data include PCDD/F releases to air, land, and water
Measurements of PCBs, PCDD/Fs, HCB air concentrations over the globe (SC GMP Data Warehouse)
Annual PCDD/F emissions to air (g I-TEQ/yr)
Measured HCB air concentrations (pg/m3)
Assessment of POP pollution: co-operation with UNEP Stockholm Convention (SC)

## Slide 19
Assessment of POP pollution and processes
Research activities related to regional and global scales:
Analysis of congener composition of emission and concentrations in media (PCDD/Fs, PCBs)
Refinement of parameterization of atmospheric transformation/removal processes and exchange with media
Further development of source-receptor methodology accounting for multi-media transport of POPs
Assessment of intercontinental transport to/from EMEP region
Multi-model study of global POP transport applying UNEP SC GMP measurement data
GLEMOS (EMEP/MSC-E)
BETR-Research (Switzerland/Sweden)
Measured and modelled PCB153 in air for the period 2004-2013, pg/m3

## Slide 20
Contribution to the UNEP SC Second Global GMP report, 2016
Multi-model assessment of POP pollution and processes
Study of global transport, phase partitioning, and media exchange
GLEMOS (MSC-E) and BETR (Sweden) models vs. measurements of UNEP SC GMP DWH
EMEP region
Notes: 20

## Slide 21
Regular pollution assessment over EMEP domain:
Substances – Pb, Cd, Hg, PAHs, HCB, PCBs, PCDD/Fs
Concentration and deposition maps
Source-receptor relationships
Long-term trends (1990-2013)
Pollution assessment on a global scale:
Substances – Hg, HCB, PCBs, PCDD/Fs
Includes the whole AMAP region
Intercontinental transport
Joint AMAP/CLRTAP workshop, Potsdam, Germany, February 2016
Cooperation with AMAP and dissemination of results
MSC-E activities relevant to the Arctic
EMEP
AMAP and EMEP domains

## Slide 22
HELCOM expressed its interest for evaluation of Baltic Sea pollution by new substances (PBDE, HBCDD, PFOS) (PRESSURE group meeting, 2015)
Assessment of atmospheric input of HMs (Pb, Cd, Hg) and POPs (PCDD/Fs, PAHs, PCBs) to the Baltic Sea
Cooperation with HELCOM and dissemination of results
Source apportionment of Cd deposition
Deposition to the Baltic Sea

## Slide 23
Work-plan elements for 2017
Work on transition of modelling system to the new EMEP grid
Further development of multi-media modelling approach for mercury
Model evaluation of POP (B[a]P) contamination of highly populated regions (urban areas)
Country specific activities on HM pollution assessment with fine spatial resolution (Case studies: Poland, UK)
Contribution to the development of emission strategy
Refinement of model parameterization of phase partitioning and inter-media exchange of POPs
Co-operation and exchange of information with different international organizations (AMAP, UNEP Minamata and Stockholm Conventions, HELCOM)

## Slide 24
Gridded emission data
areas covered
areas not covered
Temporal variations of B[a]P emissions at a particular location in Central Europe
Spatial distribution of global annual PCDD/F emissions to the atmosphere
Emission characteristics affecting assessment of pollution

## Slide 25: Multi-model study of Hg atmospheric chemistry
Seasonal variation of Hg wet deposition
Measurements
ECHMERIT
GLEMOS
GEM-MACH-Hg
GEOS-Chem
Sites measuring Hg wet deposition
0
20
40
60
80
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Wet deposition, ng/m
2
/day
99 sites
0
10
20
30
40
50
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Wet deposition, ng/m
2
/day
14 sites

## Slide 26: Multi-model study of Hg atmospheric chemistry
0
20
40
60
80
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Wet deposition, ng/m
2
/day
Hg0 + Br (Br dataset I)
0
20
40
60
80
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Wet deposition, ng/m
2
/day
Hg0 + O3
0
20
40
60
80
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Wet deposition, ng/m
2
/day
Hg0 + OH
0
20
40
60
80
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Wet deposition, ng/m
2
/day
Hg0 + Br (Br dataset II)
Seasonal variation of wet deposition (North America)
Measurements
ECHMERIT
GLEMOS
GEM-MACH-Hg
GEOS-Chem

## Slide 27
Transition to the new EMEP grid
Comparison of model simulations on new and old grids
Average Hg deposition in EMEP countries (2014)